## Slide 1: 2 Meter Copper J-Pole Antenna Build
By:
Gordon Wadey, W3DBX

## Slide 2: Antenna Build Project Goals:
Hit the N4POW Repeater
Easy to build
Easy to erect
Durable
Stealthy
Better gain than my ground plane antenna
No radials
Low angle of radiation
Wide bandwidth
Low noise

## Slide 3
https://m0ukd.com/calculators/slim-jim-and-j-pole-calculator/

## Slide 4: The N4POW Tuned Antenna Jig

## Slide 5: Rig Expert Analyzer results (SWR)

## Slide 6: Rig Expert Analyzer results (Bandwidth)

## Slide 7: Rig Expert Analyzer results (Resonance)

## Slide 8: Rig Expert Analyzer results (Parameters)

## Slide 9: Rig Expert Analyzer results (Smith Chart)

## Slide 10: Parts and Tools needed for the build
Tools / Misc.
Butane Torch
95/5 Plumbing Solder
Tubing cutter
Tape measure
Steel Wool / Sand Paper
Drill & Bit Set
Soldering Iron / Rosin Core Radio Solder
Copper J-Pole Antenna - Parts List
10’ – ½” Copper Pipe
3 - ½” Caps
1 - ½” Tee
1 - ½” Elbow
1 - ½” Slip Coupling Sleeve – No Stop!
1 - Female Type N Chassis Mount Connector
4” - No. 14 copper wire

## Slide 11: Conclusion
My Project Discoveries:
VHF has unpredictable behavior
Many system factors are in play;
  Radio
  Connector Type
  Coax type
  Coax length tuning
  Antenna tuning
Vector Network Analyzer (VNA) sequence;
  Focus on connectors and coax first
  Calibrate VNA
  “Null” the coax
  Recalibrate VNA with nulled coax
  Keep antenna well clear of solid objects
  Tune the antenna with “Nulled” coax
  Check VNA readings

## Slide 12: Thank You!!
Join me for a “hands-on” build of this antenna design on Saturday March 23rd,
at the Fighting Creek Park Pavilion at 9:00AM
Immediately following the 8:00AM PARC Fellowship Breakfast at the County Seat Restaurant
Questions? / Discussion!